PlcServer
Andrei Errapart / 56 692 469

# Introduction

PlcServer collects data from the PLC-s, stores them in the database and forwards the data to the operators (for example, Control Panel) on request.

# Usage

PlcServer is to be installed as a service in order to ensure permanent availability of the service.

PlcServer listens on the port 1503. This port should be passed through the firewall.

To manage the database, please stop the service and run the server as an ordinary program with the command line parameter “--run”.

Command line parameters:
--run	Run the server as an ordinary program.
--import DIR	Import DIR/*/setup.xml files and create corresponding “*.plc” files.

# Technical information

## Files
Files are searched for in the current directory.

Database files:
Databases are in Sqlite format. The names of the databases are as follows:
1. “*.op” - Operator database, for example, “Kasutaja.op”.
2. “*.plc” - PLC database, for example, “Ranna VTJ.plc”.

Design feature: The database structures are designed such that the separated databases do not rely on each other, i.e. they can be independently modified or even removed altogether with no ill effects.

Data is kept for a period of 100 days. Any data older than that is deleted upon:
1. Program startup.
2. PLC reconnection.

## Control protocol

TODO

## Internal structure of the server
The backbone is a MailboxProcessor<PlcServer>. Thus, all message processing is done in a single thread, which mostly removes threading and locking issues.

PlcUser:
server: PlcServer
user_info	PlcDb.PlcUser, also serves as a DB connection.

OperatorUser:
server: PlcServer
user_info:	PlcDb.OperatorUser, also serves as a DB connection.
plc_db:	Database connections, same length as server.
PlcsToMonitor	List of PLC Id-s to monitor.

Server : PlcServer
PlcUsers:	Connected users.
OperatorUsers:	Connected operators.
DbPlcUsers:	Connections to the PLC databases.
DbOperatorUsers:	Connections to the user databases.